## Slide 1: Demonstrations with physical devices
Lecture 7
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Demo – scenario 1
Demo – scenario 2

## Slide 3
Demo – scenario 1

## Slide 5
Corporate WEB and DNS Server
fa0/1
fa0/2
ge1/0/1
ge1/0/2
ge1/0/3
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
ether 1
ether 5
SSID:
NetFund-Corporate
SSID:
NetFund-Guest
Ruckus AP
ZoneFlex 7363
Cisco 3560 PoE
3COM 4500G
MikroTik
RB951Ui-2HnD
Demo - scenario 1

## Slide 6: Topology details – scenario 1
DHCP server for both VLANs is the Cisco device
MikroTik is routing the VLANs and making NAT to “outside”
Device, interface | IP address
Cisco, VLAN 5 | 10.5.5.3
Cisco, VLAN 10 | 10.10.10.3
3COM, VLAN 5 | (10.5.5.2)
3COM, VLAN 10 | (10.10.10.2)
Corporate server (Web and DNS) | 10.10.10.101
MikroTik, VLAN 5 | 10.5.5.1
MikroTik, VLAN 10 | 10.10.10.1

## Slide 7
Demo – scenario 2

## Slide 8
Corporate WEB, DNS and DHCP Server
fa0/1
fa0/2
VLAN 5 (guest): 10.5.5.0/24
VLAN 10 (corporate): 10.10.10.0/24
Internet
ether 1
ether 5
SSID:
NetFund-Corporate
SSID:
NetFund-Guest
Ruckus AP
ZoneFlex 7363
Cisco 3560 PoE
MikroTik
RB951Ui-2HnD
Demo - scenario 2
fa0/3
10.23.23.0/24
10.13.13.0/24

## Slide 9: Topology details – scenario 2
DHCP server for both VLANs is the (Windows) Server
Cisco is routing the VLANs, MikroTik is making NAT to “outside”
Device, interface | IP address
Cisco, VLAN 5 | 10.5.5.3
Cisco, VLAN 10 | 10.10.10.3
Cisco, fa0/3 | 10.13.13.3
Cisco, fa0/2 | 10.23.23.3
Corporate server (Web and DNS) | 10.13.13.101
MikroTik, ether 5 | 10.23.23.1

## Slide 10: Summary
…
…
…
Demo – scenario 1
Demo – scenario 2

## Slide 12: SoftUni Diamond Partners

## Slide 13: Educational Partners

## Slide 14: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 14