## Slide 1: Layer 2 redundancy – Spanning Tree Protocol
Lecture 4
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
Spanning tree protocol (STP)
Rapid STP (RSTP)
Per-VLAN STP plus (PVST+)

## Slide 3
Spanning tree protocol (STP)

## Slide 4: What is the Spanning Tree Protocol?
It addresses a problem which switches can not handle alone: the broadcast storms
Without STP, a L2 loop will:
    Overload the links
    Affect the end devices
    Cause MAC table instability
    …never stop

## Slide 5: What is the Spanning Tree Protocol? (2)
All STP enabled switches “talk” to each other
The management information that they exchange is in the form of BPDUs (Bridge Protocol Data Units)
The goal is to logically block one or more ports to prevent from loops

## Slide 6: Why STP is needed?
In this topology STP is NOT needed
…but there is no redundancy

## Slide 7: Why STP is needed? (2)
Now there is a redundancy
…but there is also the loop problem!

## Slide 8: The STP algorithm
Elect the Root switch (Root bridge)
    This is the switch with the lowest BID (Bridge ID)
    BID = Switch Priority and MAC
Select the root ports
    They have the best cost (lowest) to the Root
    Selected per switch
Select the designated ports
    They have the best cost (lowest) to the Root
    Selected per segment (connection)
All other ports go to blocking state

## Slide 9: STP tie-breakers
If there is a tie situation - the same path cost via different paths, use the following tie-breakers:
    When selecting Root port or Designated port, chose the neighboring switch which has the lowest Bridge ID
    If the Bridge ID is the same, select the lowest Port ID (PID)
    Port ID = Port priority and port number

## Slide 10: Link costs (path cost)
Higher port speed -> lower cost
The values can be changed by administrator

## Slide 11: STP Priority
A number between 0 and 61440
Must be configured in increments of 4096
Default is 32768 (+ the VLAN ID)
The switch with the lowest priority will become the Root
If equal values -> lowest MAC address wins (BID = Priority and MAC)

## Slide 12: STP Priority (2)
16 bits reserved for bridge priority initially
Only the first 4 are now used for priority and the other 12 are for VLAN

## Slide 13: STP Priority (3)
Extended system ID is the reason for the 4096 increments

## Slide 14: STP Example 1
Priority 0
Priority 4096
Priority 32768
All links have the same cost

## Slide 15: STP Example 2
Find the Root, the RP, the DP and the Blocking ports
Root
Rp
Rp
Rp
Dp
Dp
Dp
Dp
Dp
Dp
Fa0/1
Fa0/1
Fa0/2
Fa0/3
Fa0/2
Fa0/3
Fa0/1
Fa0/2
Fa0/3
Fa0/1
Fa0/2
Fa0/3

## Slide 16: STP Example 3
Root
Rp
Rp
Rp
Dp
Dp
Dp
Dp
Dp
Dp
Rp
Find the Root, the RP, the DP and the Blocking ports
fa0/1
fa0/2
fa0/1
fa0/2
fa0/1
fa0/2

## Slide 17
Rapid STP (RSTP)

## Slide 18: Spanning Tree Protocol – Main Flavors
STP - Spanning Tree Protocol, IEEE 802.1D
RSTP - Rapid STP, IEEE 802.1W
MSTP - Multiple STP, IEEE 802.1S (802.1Q-2005)
PVST+ - Per-VLAN STP, Cisco proprietary

## Slide 19: STP (the good old Spanning Tree)
Spanning Tree Protocol
The industry standard name is IEEE 802.1D
Slow convergence
Port states:
    Disabled
    Blocking (up to 20 sec)
    Listening (up to 15 sec)
    Learning (up to 15 sec)
    Forwarding

## Slide 20: RSTP (the faster STP)
Rapid STP
The industry standard name is IEEE 802.1W
Much faster convergence than STP
Introducing Edge port – a port which is connected to an end device
RSTP uses the same algorithm as STP
Port states:
    Discarding
    Learning
    Forwarding

## Slide 21
Per-VLAN STP plus (PVST+)

## Slide 22: PVST+
Per-VLAN Spanning Tree is Cisco protocol
Why? It has a similar idea as MSTP -
Creates a spanning tree topology separately
PortFast in PVST+ is like Edge port in STP/RSTP
to distribute the load
for each VLAN

## Slide 23: PVST+ (2)

## Slide 24: PVST+ (3)
Switch 2
Switch 3
Vlan 1
Vlan 2
Priority: 0
Priority: 4096
Priority: 32768
Priority: 32768
Priority: 0
Priority: 4096
R
R
Switch 1
Vlan 1
Vlan 2
Vlan 1
Vlan 2
port 1
port 2
port 1
port 2
port 1
port 2

## Slide 25: The good and the bad about PVST+
PVST+ advantages:
  triggers STP calculation only if there is a potential loop in a particular VLAN
  detailed “look” of the network – does not block ports when there is no loop on the trunks for a given VLAN
  PVST+ disadvantages
  generates a lot of overhead in the network
  proprietary protocol

## Slide 26
Demonstration

## Slide 27: Summary
…
…
…
Spanning tree protocol (STP)
Rapid STP (RSTP)
Per-VLAN STP plus (PVST+)

## Slide 29: SoftUni Diamond Partners

## Slide 30: Educational Partners

## Slide 31: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 31