## Slide 1: IP Services and Basic Routing
Lecture 5
Software University
http://softuni.bg
SoftUni Team
Technical Trainers

## Slide 2: Table of Contents
IP services: DHCP and DNS
Introduction to routing
Direct routing
Inter-VLAN routing
Static routing

## Slide 3
IP services: DHCP and DNS

## Slide 4: What is DHCP?
DHCP: Dynamic Host Configuration Protocol
Provides automatic distribution of IP addresses and other networking parameters such as:
    Subnet mask
    Default gateway
    DNS servers
    More…
Industry standard

## Slide 5: Why use DHCP?
Reduces the administration efforts
Easy to use from the clients
Decreases the risk of IP address duplication
Can provide additional network information
DHCP fingerprinting

## Slide 6: When NOT to use DHCP
Static IP configurations may be preferred for:
  Servers
  Network devices (switches, routers, etc.)
  Printers
  Admin stations
  Very small networks may prefer not to use DHCP at all

## Slide 7: DHCP Reservations
Alternative way to have “static” addresses with DHCP: DHCP reservations
The server gives the same IP address to the same client (MAC address) each time
Examples:
  Always assign 192.168.1.100 to 37-25-AE-6C-0C-7F
  Always assign 192.168.1.200 to 41-AA-7E-21-31-54

## Slide 8: DHCP Components
Server
    DHCP scope - range of addresses (pool), lease time, reservations, etc.
    Uses port UDP 67
Client
    Must be configured to use DHCP
    Uses port UDP 68
(Relay agent)
    Used to serve multiple (V)LANs with a single DHCP server

## Slide 9: The DHCP Process
“DORA”
  Discover
  Offer
  Request
  Acknowledge
All messages use broadcast (IPv4)

## Slide 10: DHCP Relay
Two facts about the DHCP operation and the (V)LANs:
DHCP uses broadcast and this is limited to a single (V)LAN
Multiple (V)LANs = multiple broadcast domains
So how to use DHCP in multiple (V)LANs?
Two options to serve clients from multiple broadcast domains:
  Use a separate DHCP server in each (V)LAN
  Use DHCP relay

## Slide 11: DHCP Relay (2)
Scope settings for 192.168.1.0/24
Scope settings for 172.16.23.0/24

## Slide 12: DNS Introduction
DNS: Domain Name System
DNS Usage:
    To translate names to IP addresses
    To translate IP addresses to names
    To find a particular service in the network
*DNS will be discussed in more details in the advanced course

## Slide 13: DNS “A” Records
One of the most commonly used records in DNS
Matches a hostname (or FQDN) to an IP address
Examples:
  pc1 -> 192.168.1.1
  pc2 -> 192.168.1.2
  server -> 192.168.1.100
  www.abv.bg -> 194.153.145.104
*FQDN = Fully Qualified Domain Name

## Slide 14: DNS: Client-to-Server Communication
The clients need to know the address of their DNS server(s)
It can be either:
    Statically configured
    OR
    Dynamically received from a DHCP server
  DNS uses server port 53 (both UDP and TCP)

## Slide 15
Introduction to routing

## Slide 16: Switching vs Routing
Switches:
  Use Layer 2 information (MAC addresses)
  Forwarding decisions based on the MAC address tables
  Not scalable for big networks
    Routers:
        Use Layer 3 information (IP addresses)
        Forwarding decisions based on the routing tables
        Scalable for large networks

## Slide 17: What is required for routing?
If a destination IP address is not local, the sending device consults its routing table
The routing table has entries which describe:
    Which is the destination network?
    How to reach it?
    Example:
    192.168.1.0/24 via 10.1.1.1
Destination network
How to reach it

## Slide 18: The Routing Table
My routing table:
192.168.5.0/24 via 10.1.1.1
172.16.0.0/16 via 10.15.15.1
87.15.23.0/24 via 10.23.23.1
10.1.1.0/24 is local
10.15.15.0/24 is local
10.23.23.0/24 is local
10.1.1.100
10.15.15.100
10.23.23.100

## Slide 19: Default Gateway

## Slide 20: Default Gateway (2)
My routing table:
192.168.5.0/24 is local
10.1.1.0/24 is local
172.16.0.0/16 via 10.1.1.2
87.15.23.0/24 via 10.1.1.2
10.15.15.0/24 via 10.1.1.2
10.23.23.0/24 via 10.1.1.2
OR
192.168.5.0/24 is local
10.1.1.0/24 is local
0.0.0.0/0 via 10.1.1.2 (default gateway)

## Slide 21: The Rule of the Longest Match
192.168.0.0/16 via 10.1.1.1
192.168.5.0/24 via 10.15.15.1
0.0.0.0/0 via 10.23.23.1
How do I reach 192.168.5.3?
How do I reach 192.168.18.7?
How do I reach 85.12.3.42?
Answer: via 10.15.15.1
Answer: via 10.1.1.1
Answer: via 10.23.23.1

## Slide 22
Direct routing

## Slide 23: Direct routing

## Slide 24
Inter-VLAN routing

## Slide 25: How to Route Between VLANs
To route between two or more VLANs, a Layer 3 device is required (Router or L3 switch)
Inter-VLAN routing can be done with either
    The same switch which holds the VLANs (if it is L3)
    External L3 switch
    External router
    Only IP addresses (one per VLAN) and no other static or dynamic routing configuration is required

## Slide 26: Inter-VLAN Routing Using the Same Switch
(This is L3 switch)

## Slide 27: Inter-VLAN Routing Using the Same Switch (2)
The switch must have L3 functionality
Configurations required:
    One IP address per VLAN
    Default gateway on the end devices

## Slide 28: Inter-VLAN Routing Using External Switch
Trunk ports
(This is L3 switch)
(This is L2 switch)

## Slide 29: Inter-VLAN Routing Using External Switch (2)
The external switch must have L3 functionality
Configurations required:
    Trunk ports for the switch-to-switch connection
    One IP address per VLAN on the external switch
    Default gateway on the end devices

## Slide 30: Inter-VLAN Routing Using External Router
Trunk port

## Slide 31: Inter-VLAN Routing Using External Router (3)
Known as “Router on a stick” or “One-armed router”
Configurations required:
    Trunk port on the switch
    Sub-interfaces on the router (with “encapsulation dot1Q vlan”)
    One IP address per sub-interface
    Default gateway on the end devices

## Slide 32
Static routing

## Slide 33: Direct vs indirect Routing
Directly connected networks (or VLANs) does not require static or dynamic routing configuration
To reach remote networks, entries in the routing tables must be added – this is known as indirect routing
The routing table can be updated
    Statically (manual configuration)
    Dynamically (requires routing protocol like OSPF)

## Slide 34: Static Routes
10.1.1.0/24 is local
192.168.1.0/24 is local
192.168.2.0/24 via 192.168.1.2
10.2.2.0/24 via 192.168.1.2
192.168.1.0/24 is local
192.168.2.0/24 is local
10.1.1.0/24 via 192.168.1.1
10.2.2.0/24 via 192.168.2.3
192.168.2.0/24 is local
10.2.2.0/24 is local
10.1.1.0/24 via 192.168.2.2
192.168.1.0/24 via 192.168.2.2

## Slide 35
Demonstration

## Slide 36: Summary
…
…
…
IP services: DHCP and DNS
Introduction to routing
Direct routing
Inter-VLAN routing
Static routing

## Slide 37: Questions?
Notes: 37

## Slide 38: SoftUni Diamond Partners

## Slide 39: Educational Partners

## Slide 40: Trainings @ Software University (SoftUni)
Software University – High-Quality Education, Profession and Job for Software Developers
  softuni.bg, about.softuni.bg
Software University Foundation
  softuni.foundation
Software University @ Facebook
  facebook.com/SoftwareUniversity
Software University Forums
  forum.softuni.bg
Notes: 40